## Slide 1
Lecture On:
Acoustic Metamaterials
Ryan Hill

## Slide 2
Types of Waves – Transverse Wave

## Slide 3
Types of Waves – Sound Pressure (Longitudinal) Wave
At time t = 0
At time t =
http://hyperphysics.phy-astr.gsu.edu/hbase/Sound/tralon.html
No mean particle displacement
  The sound wave oscillates the particles back and forth
Increasing Pressure leads to increasingly dense particles
Decreasing Pressure leads to decreasingly dense particles
Equilibrium Pressure is Atmospheric Pressure

## Slide 4
Types of Waves – Sound Pressure (Longitudinal) Wave
http://www.indiana.edu/~emusic/etext/acoustics/chapter1_sound3.shtml

## Slide 5
What is Pressure?
Pressure (P)
  Normal force exerted by a fluid per unit area
  Units: Pascal (Pa)  [Pa = N/m^2]
Force
Force
Pressure
Greater
(Less Area)
Pressure
Less
(More Area)
Absolute Pressure
Atmospheric Pressure (Equilibrium Pressure
Gauge Pressure (Acoustic Pressure)
https://www.nuclear-power.net/nuclear-engineering/thermodynamics/thermodynamic-properties/what-is-pressure-physics/

## Slide 6
C (Speed of Sound of Gases)
General equation of state, define the speed of sound as:
Bulk modulus
  ”of a substance is a measure of how resistant to compression that substance is”
  “the ratio of the change of volume (thus, the density) of a given mass of fluid/solid
when there is a change in pressure”
For Ideal Gas Conditions,
Temperature dependent
https://nigerianscholars.com/tutorials/friction-drag-elasticity/changes-in-volume-bulk-modulus/

## Slide 7
C (Speed of Sound of Gases)
Temperature dependent
How does the value of Humidity change the Molecular Weight?
Humidity (H)
  is the amount of water vapor (gas) in the air.
Relative Humidity (RH)
  is the amount of water vapor in the air to the total amount of water vapor that be held in the air at a temperature
  “ is the ratio of the partial pressure of water vapor to the equilibrium vapor pressure of water at a given temperature”
Humidity dependent

## Slide 8
Linear Euler Wave Equation
Linear Euler’s Wave Equation
  Valid for acoustic processes of small amplitudes and no viscosity
    Solution:
A Solution to the Linear Euler’s Wave Equation, when the wave is a plane wave
Plane Wave

## Slide 9
Pressure, Velocity, and Impedance (Ohm’s Law Equivalent)
  Used for determining transmission
Ohm’s Law Analogy
Example: For Plane Wave
Volume Velocity = Volume flow rate
https://slideplayer.com/slide/8336241/

## Slide 10
Acoustic Transmission Line Model
https://mycourses.aalto.fi/pluginfile.php/395000/mod_resource/content/1/Lecture10.pdf

## Slide 11
S-Parameters (Complex Systems)
S-Parameters for a complex system consist of the transfer matrix for each component of the system
The Transfer matrix for a pipe with the same impedance as well as the same cross sectional area is:
Example of an Expansion Chamber that is in the middle of a pipe
https://mycourses.aalto.fi/pluginfile.php/395000/mod_resource/content/1/Lecture10.pdf
Note: q is velocity, v, for this example
Type equation here.
http://web.engr.uky.edu/~dherrin/ME510_Old/Chapter_10_Sound_in_Ducts.pdf

## Slide 12
S-Parameters (Side Branch and Helmholtz Resonator)
By Continuity of Pressure,
Also,
We know
Thus,
The Transfer matrix is
To find the transfer matrix for a side branch that is a Helmholtz resonator, just solve for the impedance , which is the
impedance of the Helmholtz Resonator
http://web.engr.uky.edu/~dherrin/ME510_Old/Chapter_10_Sound_in_Ducts.pdf

## Slide 13
Helmholtz Resonator
What is a Helmholtz Resonator?
  A cavity containing a fluid (usually air) with a hole in the cavity, where a neck is attached.
    The neck allows flowing fluid to enter the cavity.
    This is the phenomena that occurs when blowing over a glass bottle is a result of the bottle being a Helmholtz Resonator.
      C = Speed of Sound in Medium
      V = Volume of the Resonator Cavity
      S = Cross Sectional Area of the Neck
      = Length/Height of the Neck
      = Neck Length Adjustment, based on whether the neck is flanged
https://newt.phys.unsw.edu.au/jw/Helmholtz.html

## Slide 14
Acoustic Metamaterials
Properties changed by Acoustic Metamaterial
  Bulk Modulus, k,
  Mass Density,
Similar to EM metamaterials, Acoustic Metamaterials create properties that are not naturally negative
Acoustic Metamaterials can create things, such as:
  Enhanced Absorbers
  Enhanced Transmitters
  Slowed Sound Waves
  Superlens
  Negative Refraction
  Polarized Sound Waves
  Acoustic Diode
  Acoustic Multiplexer
  Acoustic Split Ring Resonator
  Sonic Crystals
Acoustic Metamaterial Classification
Refraction is the bending of waves when they enter a medium where their speed is different.
https://physicstoday.scitation.org/doi/10.1063/PT.3.3198

## Slide 15
Acoustic Metamaterial Unit Cell (Helmholtz Resonator)
An Acoustic Metamaterial is made up of unit cells containing one or more structures that effect the acoustic wave
    One of the most common structures is a Helmholtz Resonator
Each unit cell has an effective bulk modulus and effective mass density.
Each unit cell has there own transmission loss and other properties.
Total of all the unit cells is what makes up the Acoustic Metamaterial
Example: Acoustic Metamaterial Unit Cell Properties
Metamaterial
Non-
Metamaterial
Metamaterial
Metamaterial
Non-Metamaterial
Non-Metamaterial
Unit Cell
https://www.researchgate.net/publication/325104291_Benchmark_Analysis_of_a_Helmholtz_Resonator_for_Estimating_Acoustic_Metamaterial_Properties

## Slide 16
Old Experimental Lab Setup
Drawback to this setup
  Hard to measure the Transmission Loss, usually
  measured the Insertion Loss, instead.
  The REFLECTIONS, especially at lower frequencies

## Slide 17
From BSWA Impedance Tubes product literature, version 201008
BSWA Impedance Tube
Diameter of Impedance Tube | 100 [mm] | 30 [mm]
Part Number | SW422 | SW477
Operating Frequency | 63[hz] – 1600 [hz] | 1000 [hz] – 6100 [hz]
BSWA SW422 Impedance Tube
BSWA SW477 Impedance Tube
Sample
Holder
Speaker
Microphones
Speaker

## Slide 18
Impedance Tube Measurement Setup
Note: End of tube can be terminated with hard, soft, anechoic, or no boundary, depending on the type of measurement, and following e.g. ASTM procedures.

## Slide 19
Nothing in the Impedance Tube
Transmission Loss
The S-Parameters for an empty Impedance Tube:

## Slide 20
Metamaterial Sample
Metamaterial Sample Specifications
  Face Diameter: 100 [mm]
  Depth: 50 [mm]
  Resonance Frequency: ~983, ~1025 [Hz]
  Sample Shows
    TL Peak of 44 dB @ ~1006 [Hz]
    Satellite TL Peak of 33 dB @ ~976 [Hz]
Metamaterial Sample
100 mm
Transmission Loss of New Sample