## Slide 1
Applications of Acoustic Metamaterials: Noise Reduction
Presented By: Ryan Hill & Ed Stokes
University of North Carolina at Charlotte
Ed Stokes, ECE Professor
Ryan Hill, ECE Graduate Student
Matias Mendieta, ECE Undergraduate Student
Patrick Bruce, ECE Undergraduate Student

## Slide 2: Outline
Co-funding and Center I.P.
Case study: Characterization of fan noise
Experimental Setup
Modeling (Comsol Multi-Physics)
Measurements on Large Helmholtz Resonators
Design and fabrication of coupled H.R. arrays
Initial test results
Future: Acquisition of 4 mic impedance tube

## Slide 3: Co-funding & Center I.P.
Project in 2017-18 was funded by Center for Metamaterials
Arrays of miniature coupled Helmholtz resonators is probably a patentable concept
  Especially if coupled with specific applications.
We are moving toward functional prototypes.
Appropriate patent application(s) will be filed as results are demonstrated.

## Slide 4
Need and Relevance: Objectives
Develop Acoustic Metamaterial structures to absorb noise e.g. cooling fans in electronic systems.
  Would like to use Helmholtz resonators with small geometry to filter fan noise (~800Hz) frequencies
  However, H.R. size is larger for lower frequencies
  Therefore, size optimization is critical for miniature arrays
Eventually, the design methodology will be applied to other applications.

## Slide 5
Typical Cooling Fan Data
  Seven Fan Blade at 7200 RPM
Peak # | What is it? | Calculated | Measured
1 | FRF Harm. #1 | 117 Hz | 115 Hz
2 | BPF Harm. #1 | 817 Hz | 803 Hz
3 | ??? | N/a | 1377 Hz
4 | BPF Harm. #2 | 1634 Hz | 1606 Hz
5 | BPF Harm. #3 | 2451 Hz | 2408 Hz
6 | BPF Harm. #4 | 3268 Hz | 3209 Hz
7 | BPF Harm. #5 | 4085 Hz | 4011 Hz

## Slide 6
Notable Capabilities of the Lab
  “Quiet Box” – ETX Lindgren SD Acoustic Chamber
    Dimensions: 28 X 26 X 28 inches
    Testing Frequency: > 500 Hz
  U8903B Agilent Audio Analyzer
    2 Generators, 2 Analyzers
      10 kHz – 80 kHz (+/- 0.0005 %)
  (3) Measurement Microphones
    Frequency Response: 20 Hz – 20 kHz
    Omnidirectional Polar Pickup Pattern
    Flat Response
  (2) Avantone Mixcube Active Full-Range Reference Monitor
    Frequency Response: 50 Hz – 17 kHz
  (Future) BSWA Impedance Tube System
    Measured Frequency Range: 63 Hz – 6.1 kHz

## Slide 7
Helmholtz Resonator Equation and Design
  C = Speed of Sound in Medium
  V = Volume of the Resonator Cavity
  S = Cross Sectional Area of the Neck
  = Length/Height of the Neck
  = Neck Length Adjustment, (based on whether the neck is flanged)
    = = Rayleigh Outside & Inside End Correction
    Rayleigh Outside & Inside End Correction =
  Constraints:
What physical object is my Helmholtz Resonator Model based on (for large scale experiments)?
  A Chemical Flask
  Dimensions of the Flask:
    Resonator Volume ~= 46.51 mL
    Neck Length ~= 10 cm
    Neck Radius ~= 0.35 cm
Approach:
Assume the HR neck remains a constant value and only vary the geometry that controls the HR cavity volume
For large scale experiments, add or remove water from the flask to change the cavity volume
Take the constraints into account when designing the Acoustic Metamaterial.

## Slide 8
Experimental Lab Setup
(Single Resonator)

## Slide 9
Single Resonator Results
Using the chemical flask as the resonator
Changed the volume of the Resonator’s cavity by adding water
Theoretical Resonance Frequency curve based on Cavity volume
% of Cavity filled w/ Water | Calculated Resonance Frequency | Measured Resonance Frequency | Percent Error
0 % | 175 Hz | 187 Hz | 6.85 %
20 % | 196 Hz | 206 Hz | 5.10 %
40 % | 226 Hz | 234 Hz | 3.54 %
50 % | 248 Hz | 254 Hz | 2.42 %
60 % | 277 Hz | 282 Hz | 1.81 %
80 % | 392 Hz | 387 Hz | -1.28 %
100 % | N/A (INF) | 459 Hz | N/A

## Slide 10
Experimental Lab Setup
(Coupled Resonators)
Physical Coupled Resonator Setup
Comsol Coupled Resonator Model
Resonators Cavity Dimensions (COMSOL):
Physical
Coupled Resonator Model

## Slide 11
Coupled Resonator Results
Chart: Small Open Pipe (Diameter = 1.5 [in])
Coupled Resonance Frequencies for Helmholtz Resonators |  |  |  | 
Cavity Volume % Full | Single Resonator (HZ) (Calculated | Coupled w/ Empty (Hz) (Calculated) | Measured (Hz) | % Error of Measured
0% | ~170 | ~170 | ~166 | -2.35 %
70% | ~308 | ~239 | ~329 | +6.82 %
80% | ~377 | ~273 | ~391 | +3.71 %
90% | ~534 | ~352 | ~501 | -5.81 %
Coupled Resonance Frequencies for Helmholtz Resonators |  |  |  | 
Cavity Volume % Full | Single Resonator (HZ) (Calculated | Coupled w/ Empty (Hz) (Calculated) |  | % Error of Measured
0% | ~170 | ~170 | ~166 | -2.35 %
70% | ~308 | ~239 | ~329 | +6.82 %
80% | ~377 | ~273 | ~391 | +3.71 %
90% | ~534 | ~352 | ~501 | -5.81 %
% of Cavity Full | Color in Graph | Calculated | COMSOL Simulated | % Error
0 (Empty) | Black | ~170 | ~166 | +2.35 %
70 | Blue | ~308 | ~303 | -1.62 %
80 | Red | ~377 | ~364 | -3.45 %
90 | Green | ~534 | ~477 | -10.67 %
% of Cavity Full | Color in Graph |  |  | % Error
0 (Empty) | Black | ~170 | ~166 | +2.35 %
70 | Blue | ~308 | ~303 | -1.62 %
80 | Red | ~377 | ~364 | -3.45 %
90 | Green | ~534 | ~477 | -10.67 %
Notes: Critical Coupling Condition -

## Slide 12
Coupled Resonators: Hybrid Resonance
The Hybrid Resonance,
  The result of Quasi-Trapped Modes
  Occurs, when the reflection coefficient zero is down shifted to the real axis (seen in the figure) and becomes physically visible
  is the frequency where crosses or comes very to the real axis
In our case:
  The Quasi-Trapped mode is an Electromagnetic Induced Transparency (EIT) like mode
Critical Coupling Condition
  Analogous to point of maximizing absorption fulfilled when:
    The leakage of energy out of a resonator is equal to the inherent energy loss (Viscothermal effects at the walls)

## Slide 13
Example of Acoustic Metamaterial Design: miniature 3D-printed H.R. Arrays
Side View of Cell
Front View of Cell
Resonators
Air Flow Channel (Waveguide)
We have so far built several of these with varying levels of complexity.

## Slide 14
Acoustic Metamaterial
(v2.0) Results
Helmholtz Resonance Frequencies (V2.0) |  | 
(Theory) | (Theory) | (Theory)
3450 [Hz] | 1666 [Hz] | 2558 [Hz]
Helmholtz Resonance Frequencies (V2.0) |  | 
3450 [Hz] | 1666 [Hz] | 2558 [Hz]
Chart: Ref. Grid and Grid
Chart: Grid – Ref. Grid
Grid V2
Ref. Grid V2
Results are currently under interpretation. Need impedance tube for better testing.

## Slide 15
Characterized noise spectrum of benchmark cooling fan
Acquired lDS-Lindgren “quiet box” (University) and Agilent U8903B audio analyzer (CfM grant).
Acquired and developed Comsol Multiphysics acoustic simulation capabilities.
Developed simulation + theory + experiment for large single and coupled Helmholtz resonators (H.R.)
Designed (Solid-Works), fabricated (3D-printing) , and tested several prototype miniature coupled H.R. arrays.
Most recently, we pooled residual CfM funding with University year-end funding to acquire 4 mic impedance tube measurement system for 2018-19.
Outcomes & Deliverables
2017-2018

## Slide 16
Technology Transfer To the
Companies
We had teleconferences with Harris:
  August 2017: Discussed project details and requirements
  September 2017: Discussed Fan Noise Frequencies and Basic Theory of Resonator Filter
  November 2017: Discussed Acoustic Metamaterial Design using Helmholtz Resonators and Simulation Results
  March 2018: Discussed the experimental results of the Fabricated Acoustic Metamaterial (V1.1) and other experimental results

## Slide 17
Summer 2018: Receive and commission BSWA 4 microphone impedance tube measurement system.
Summer and fall 2018: Design, simulate, and test further iterations of miniature coupled H.R. flow cells.
Fall 2018: Optimize flow cells for fan noise (and other applications?)
Fall 2018 and Spring 2019: File patent applications.
Spring 2019: Publish results (after patent applications are filed).
Impact
Schedule
Next: After novel 3D-printed coupled H.R. arrays are successfully demonstrated, file appropriate patent applications.
    Caveat: H.R. themselves are not patentable. However, application-specific coupled arrays of miniature H.R. flow cells may be patentable.
After patent applications are filed, publish results
Students
  Ryan Hill, MSEE Spring 2019
  Matias Mendieta and Patrick Bruce, BSEE Spring 2019

## Slide 18
2017-2018 Budget
Budget justification:
* Comsol Multiphysics acoustics module
# Agilent audio analyzer, and BSWA impedance tube system
Direct Cost |  | Actual expenses
Student Salary & Benefits |  | 14,586
Tuition |  | 7,098
Supplies & Materials |  | 789
Travel |  | 1,285
Software* |  | 1,807
Equipment# |  | 10,799
Subtotal |  | 36,364
Indirect Cost |  | 
Overhead 10% |  | 3,636
Total |  | 40,000
Notes: This is an example budget

## Slide 19
Proposed 2018-19 Budget
Budget Justification: * Comsol “Live Link” for Solid Works
Direct Cost |  | Requested Support
Student Salary & Benefits |  | 20,000
Tuition |  | 8,000
Supplies & Materials |  | 1,874
Software* |  | 1,990
Travel |  | 2,500
Equipment |  | 1,000
Publication |  | 1,000
Subtotal |  | 36,364
Indirect Cost |  | 
Overhead 10% |  | 3,636
Total |  | 40,000
Notes: This is an example budget

## Slide 20
Single and multiple Helmholtz resonators (H.R.) can be accurately simulated using Comsol Multiphysics and employed for noise reduction at specific frequencies
Miniature arrays of H.R. flow cells can be:
  designed using SolidWorks
  fabricated using 3D-printing
  simulated using Comsol
However, the current measurement system is inadequate to the task of full characterization due to uncontrolled environmental reflections of acoustic waves
Newly acquired 4 microphone impedance tube system will allow further development in 2018-19
Conclusions

## Slide 21
Acknowledgements
This work was supported by the NSF Industry/University Cooperative Research Center for Metamaterials.
http://www.centerformetamaterials.org/
http://www.nsf.gov/
Notes: Can insert additional logos and acknowledgements

## Slide 22
Helmholtz Equation Adjusted
Adjusted HR Equation
  C = Speed of Sound in Medium
  V = Volume of the Resonator Cavity
  S = Cross Sectional Area of the Neck
  L = Cavity Length
  = Length of the neck
  Rayleigh Outside End Correction =
  Ingrad’s Inside End Correction
  = = )) For
The classical HR equation (for Cylinder Cavities) is the solution to the following transcendental equation:
    Approximated with Taylor series to one term
The classical HR equation (for Cylinder Cavities) breaks down when
The Classical HR equation for other shapes have a similar transcendental equation, which restricts the accuracy of the equation to the number of terms used to approximate Cot
The accuracy of the HR equation is also restricted to the neck end corrections
    Ingrad’s Inner End Correction is shown to be the more accurate equation when

## Slide 23
Coherent Perfect Absorption
And
Critical Coupling Condition
Coherent Perfect Absorption (CPA)
  Total Perfect Absorption occurs when absorption coefficient,
  Can be achieved by fulfilling the Critical Coupling Condition
Critical Coupling Condition
  Analogous to point of maximizing absorption (Open-Resonator Theory)
  Fulfilled when:
    The leakage of energy out of a resonator is equal to the inherent energy loss (Viscothermal effects at the walls)
        This is achieved by adjusting the resonator’s geometry, which controls
Notes: Critical Coupling Condition -

## Slide 24
Complex Frequency Plane
And
Reflection Coefficient
Complex Reflection Coefficient
  Form:
  Pole of Coefficient at , where
  Zero of Coefficient at , where
  Zeros at or close to the real frequency axis represent quasi-trapped modes.
For Lossless case:
  **
Fig. Example of Reflection Coefficient plotted on Complex Frequency Plane
(lossless case)
For Lossy case:

## Slide 25: Sources of Fan Resonance
Sources of Fan Resonance
1.) Fan Rotation Frequency (SBRF)
Fan RPM / 60 (s/min) = 7000 RPM / 60 (s/min) = 117 Hz
2.) Blade Pass Frequency (BPF)
BPF = [( (No. of Blades) * Fan RPM) 60 (s/min)] = 817 Hz
BPF Harmonics | 817 Hz | 1634 Hz | 2451 Hz | 3268 Hz
Sleeve Bearing

## Slide 26: Coupled Resonator Results (Hard B.C.)
% of Cavity Empty | Calculated | Measured | % Error
100 (Empty) | ~168 | ~181 | +7.73 %
30 | ~308 | ~312 | +1.29 %
20 | ~377 | ~367 | -2.6 %
10 | ~534 | ~487 | -8.8 %
% of Cavity Empty |  |  | % Error
100 (Empty) | ~168 | ~181 | +7.73 %
30 | ~308 | ~312 | +1.29 %
20 | ~377 | ~367 | -2.6 %
10 | ~534 | ~487 | -8.8 %
Chart: Small Pipe (Diameter = 1.5 [in]) with Hard Boundary Condition
Hybrid Freq | 0 | 0 | 0
# | Closed-Ended Pipe Resonances [Hz]
1 | 281.38
2 | 844.15
3 | 1406.9
4 | 1969.68
5 | 2532.42
# | 
1 | 281.38
2 | 844.15
3 | 1406.9
4 | 1969.68
5 | 2532.42

## Slide 27
Resonator Dimensions
Waveguide Dimensions
Varying , while keeping all other dimensions the same.

## Slide 28
[cm] | [Hz] | [Hz] | [cm] | [cm] | >
2 | 800 | 855 | 2.51 | 3.27 | True
4 | 622.97 | 652 | 3.26 | 3.27 | True
6 | 527.69 | 537 | 3.97 | 3.27 | False
8 | 465.97 | 465 | 4.61 | 3.27 | False
2 | 800 | 855 | 2.51 | 3.27 | True
4 | 622.97 | 652 | 3.26 | 3.27 | True
6 | 527.69 | 537 | 3.97 | 3.27 | False
8 | 465.97 | 465 | 4.61 | 3.27 | False
The simulated resonance frequency diverges from calculated resonance frequency between = 6 and 7 cm.
    The divergence of the calculated and simulated frequency could be due to the limitation of the classical HR equation (the equation diverges at )
The simulated resonance frequencies are greater than the calculated resonance frequencies, except around = 8 cm.
Simulation Results

## Slide 29: Coupled Resonators Simulation Setup
Resonator #1 Dimensions
Resonator #2 Dimensions
Waveguide Dimensions
For =
For !=
Waveguide Dimensions
Resonator #1 Dimensions
Resonator #2 Dimensions
The coupled resonator simulation is run for two cases:
  Where both resonators have the same resonance frequency
  Where the resonators have different resonance frequencies
For each case, the neck length of both resonators are varied.

## Slide 30: Coupled Resonators =
= [cm] | = [Hz] | = [Hz] | Frequency Difference (Simulated – Calculated) | [cm] | >
2 | 800 | 780 | -20 [Hz] | 2.74 | True
4 | 622.97 | 593 | -29.97 [Hz] | 3.62 | False
6 | 527.69 | 493 | -34.69 [Hz] | 4.34 | False
8 | 465.97 | 425 | -40.97 [Hz] | 5.04 | False
 |  |  | Frequency Difference (Simulated – Calculated) |  | 
2 | 800 | 780 | -20 [Hz] | 2.74 | True
4 | 622.97 | 593 | -29.97 [Hz] | 3.62 | False
6 | 527.69 | 493 | -34.69 [Hz] | 4.34 | False
8 | 465.97 | 425 | -40.97 [Hz] | 5.04 | False
The simulated resonance frequency is not equal to the calculated resonance frequency and they start to converge as becomes smaller.
The simulated resonance frequency is below the calculated resonance frequency as predicted by Johansson when coupling is occurring.
    Johansson said
    The differences between the calculated and simulated are not due to error from the classical HR formulas
There is only one resonance peak for each variation of and as Johansson stated would be the case.
Simulation Results

## Slide 31: Coupled Resonators !=
= [cm] |  |  |  |  | Difference between calculated resonance | Difference between simulated resonance
2 | 800 | 757 | 900 | 860 | 100 [Hz] | 103 [Hz]
4 | 622.97 | 580 | 701.34 | 657 | 79 [Hz] | 77 [Hz]
6 | 527.69 | 482 | 594.08 | 540 | 67 [Hz] | 58 [Hz]
8 | 465.97 | 421 | 524.59 | 465 | 59 [Hz] | 44 [Hz]
 |  |  |  |  | Difference between calculated resonance | Difference between simulated resonance
2 | 800 | 757 | 900 | 860 | 100 [Hz] | 103 [Hz]
4 | 622.97 | 580 | 701.34 | 657 | 79 [Hz] | 77 [Hz]
6 | 527.69 | 482 | 594.08 | 540 | 67 [Hz] | 58 [Hz]
8 | 465.97 | 421 | 524.59 | 465 | 59 [Hz] | 44 [Hz]
= [cm] |  |  | Frequency Difference (Simulated – Calculated) |  |  | Frequency Difference (Simulated – Calculated)
2 | 800 | 757 | -43 [Hz] | 900 | 860 | -40 [Hz]
4 | 622.97 | 580 | -42.97 [Hz] | 701.34 | 657 | -44.34 [Hz]
6 | 527.69 | 482 | -45.69 [Hz] | 594.08 | 540 | -54.08 [Hz]
8 | 465.97 | 421 | -44.97 [Hz] | 524.59 | 465 | -59.59 [Hz]
 |  |  | Frequency Difference (Simulated – Calculated) |  |  | Frequency Difference (Simulated – Calculated)
2 | 800 | 757 | -43 [Hz] | 900 | 860 | -40 [Hz]
4 | 622.97 | 580 | -42.97 [Hz] | 701.34 | 657 | -44.34 [Hz]
6 | 527.69 | 482 | -45.69 [Hz] | 594.08 | 540 | -54.08 [Hz]
8 | 465.97 | 421 | -44.97 [Hz] | 524.59 | 465 | -59.59 [Hz]
According to Johansson,
  The coupled higher pitch is higher and the coupled lower pitch is lower than the uncoupled ones.
      >
  The difference between the coupled pitch and uncoupled pitch becomes larger as the difference between the uncoupled resonant frequencies decreases.
The coupled lower pitch is lower but the coupled higher pitch is Not higher.
As the difference between the uncoupled resonance becomes smaller, as seen in table 1, the larger the difference between the coupled and uncoupled pitches become, as seen in table 2.

## Slide 32: Coupled Resonators != (Continued)
= [cm] |  |  | Frequency Difference (Simulated – Calculated) |  |  | Frequency Difference (Simulated – Calculated)
2 | 800 | 757 | -43 [Hz] | 900 | 860 | -40 [Hz]
4 | 622.97 | 580 | -42.97 [Hz] | 701.34 | 657 | -44.34 [Hz]
6 | 527.69 | 482 | -45.69 [Hz] | 594.08 | 540 | -54.08 [Hz]
8 | 465.97 | 421 | -44.97 [Hz] | 524.59 | 465 | -59.59 [Hz]
 |  |  | Frequency Difference (Simulated – Calculated) |  |  | Frequency Difference (Simulated – Calculated)
2 | 800 | 757 | -43 [Hz] | 900 | 860 | -40 [Hz]
4 | 622.97 | 580 | -42.97 [Hz] | 701.34 | 657 | -44.34 [Hz]
6 | 527.69 | 482 | -45.69 [Hz] | 594.08 | 540 | -54.08 [Hz]
8 | 465.97 | 421 | -44.97 [Hz] | 524.59 | 465 | -59.59 [Hz]
Some signs of coupling have been noted, in the previous slide.
There are no hybrid frequencies in the results, but this could be due to the Comsol model not taking into account the Thermoviscosity.
The simulation results shown to the left, look similar to a coupled EIT-like mode, similar to that seen on slide 6.
Simulation Results